## Slide 1
Automated Condensate Partition Coefficient Pipeline
Spring 2026 Progress — Week 7
Daniel Chang · Franco Lab · C&S BIO 199/197
May 7, 2026

## Slide 2
Since Last Meeting (April 22)
1. Confirmed reference PC uses background subtraction → added to pipeline
2. Built spring_implementation/pipeline.py (full Cellpose 3, 3D end-to-end)
3. Fixed nuclei over-segmentation with 3D connected-component relabeling
4. Solved dilute density instability → lowest-50-patch selection
5. Single-ROI result: PC = 6.297 vs reference 6.32 (−0.4% error)
6. Batch validation across 30 JABr cells → r = 0.735, RMSE = 2.815, bias = +2.8%
7. Discovered Cellpose over-draws boundaries → top-75% voxel trim as fix

## Slide 3
Pipeline Overview (pipeline.py)
1 Load
Condensate (Ch2) + Nuclei (Ch1) TIF stacks | 55 × 185 × 259 px
2 Denoise
Cellpose 3 DenoiseModel on every Z-slice → sharper boundaries (raw pixels unchanged — denoising only guides masks)
3 Segment
Cellpose 3 cyto3, do_3D=True → full 3D tracking Nuclei post-proc: binary mask → 3D connected components → drop noise 76 Cellpose labels → 5 clean nuclei
4 Measure
regionprops_table: area, centroid, mean intensity per object per Z
5 3D Volume
Count voxels per label across all 55 slices
6 PC
Background-subtracted Fabrini formula cond_density = mean top-75% bright voxels in cond ∩ nuc mask dil_density = mean of 50 lowest-intensity 10×10×10 patches in dilute region PC = cond_density / dil_density

## Slide 4
Single-ROI Validation (Sample2_5_1)
PC = 6.297
Reference = 6.32 (−0.4% error)
Three improvements that closed the gap (3.3 → 6.3):
Background subtraction (April 25) — reference was bg-subtracted; pipeline wasn't. Largest single jump.
Connected-component nuclei relabeling (April 30) — 76 Cellpose fragments → 5 true nuclei. Fixes dilute-phase pixel coverage.
Lowest-50-patch dilute density (April 30) — replaces unstable single random patch (PC swing: 4.3–6.0 across seeds).

## Slide 5
Key Finding: Cellpose Over-draws Boundaries
Diagnosis (Sample3_3_11, ref PC = 16.95):
Pipeline cond density: 466 → pipeline PC = 8.32
Reference cond density: 1362 → reference PC = 16.95
Cellpose 3D masks include bright core + large dim halo + dark interior pixels.
Manual Imaris boundaries capture only the bright core.
Variant
r
RMSE
Bias
top-10%
0.912
13.10
+120%
top-25%
0.865
8.17
+75%
top-50%
0.783
3.93
+30%
top-75% ✓
0.735
2.82
+3%
full mean
0.716
3.25
−16%
top-75% trims the ~25% 'fluff' Cellpose adds beyond a manual boundary. Near-zero bias and best RMSE across 29 cells.

## Slide 6
Batch Validation — 30 JABr Cells
0.735
Pearson r
2.815
RMSE
+2.8%
Mean bias
29 / 30
Cells processed
Well-calibrated cells (error < 5%)
Sample1_1_3 ref=19.77 pipe=19.90 (+0.7%)
Sample3_3_3 ref=8.82 pipe=8.74 (−1.0%)
Sample3_3_7 ref=8.68 pipe=8.55 (−1.5%)
Sample1_4_1 ref=6.13 pipe=6.20 (+1.1%)
Sample3_3_9 ref=5.92 pipe=6.13 (+3.6%)
Known failures (segmentation, not calibration)
Sample1_1_1 +146% wrong cell selected
Sample3_3_2 −51% missed nucleus
Sample3_3_11 −38% bright cores undersampled
Sample2_5_5 −38% large FOV, nucleus not detected
Sample3_3_15 NaN zero condensate in central nuc

## Slide 7
Per-Cell Results: Reference vs Pipeline (top-75%)
Sample
Reference PC
Pipeline PC (top-75%)
Error
Sample1_1_3
19.77
19.90
+0.7%
Sample1_4_3
13.96
13.04
−6.6%
Sample3_3_3
8.82
8.74
−1.0%
Sample3_3_7
8.68
8.55
−1.5%
Sample3_3_1
8.18
8.31
+1.5%
Sample3_3_9
5.92
6.13
+3.6%
Sample1_4_1
6.13
6.20
+1.1%
Sample3_3_11
16.95
10.57
−38.0%
Sample3_3_2
9.05
4.47
−50.6%
Sample2_5_5
6.73
4.20
−37.6%
Sample1_1_1
4.78
11.77
+146%
Sample3_3_15
6.41
NaN
NaN
Well-calibrated
Segmentation failure

## Slide 8
Outstanding Issues
Nuclei over-segmentation
Cellpose still labels each nucleus as ~15–25 fragments internally. Connected-component fix makes the binary mask correct, but true fix would need 2D+stitch or a custom-trained model.
top-75% not universally optimal
Calibrated for JABr. If Cellpose draws tighter masks on other constructs (JwtBr, 10ntABr), trimming 25% may over-correct. Would need per-cell mask quality assessment to tune adaptively.
Single-cell selection heuristic
Central nucleus works for well-cropped ROIs. Fails on wide-FOV images (Sample2_5_5: 32×417×370) where the target cell isn't centered.
Sample3_3_15 NaN
Central nucleus has zero condensate overlap. Need fallback selection (e.g. max-overlap nucleus) when central nucleus is empty.

## Slide 9
Discussion & Next Steps
Questions to discuss:
Is top-75% voxel trimming a defensible method to report in the paper, or should we pursue tighter segmentation instead?
Run batch_compare on other constructs (JwtBr, 10ntABr) to test generalizability?
Outlier cells (Sample2_5_5, Sample3_3_15) — worth fixing, or exclude with justification?
Poster / report scope — what level of batch validation is enough?
Planned next steps:
Run batch_compare on JwtBr / 10ntABr constructs
Fix Sample3_3_15 NaN: add fallback nucleus selection
Add discussion + applicability slides to presentation
Explore 2D+stitch approach for nuclei segmentation (if time permits)